## Slide 1: Paper 197: A Novel Sensitivity Analysis Method Using Self-Organizing Maps (SOM) Deepanshu and Palaniappan Ramu
15th World Congress on Structural and Multidisciplinary Optimization | WCSMO 2023
$Advanced Design, Optimization, & Probabilistic Techniques (ADOPT) Laboratory
Department of Engineering Design
Indian Institute of Technology Madras
Chennai, India

## Slide 2: Content
Sensitivity Analysis
Current Challenges
  Curse of Dimensionality
  Limited Budget
  Discontinuity
Self-Organizing Map (SOM)
SOM for Meta-modeling
SOM for Sensitivity Analysis
Results and Discussion
Summary and Future Work

## Slide 3: Surrogate-assisted Sensitivity Analysis
Sensitivity Analysis:
Sensitivity analysis is the study of how the ‘outputs’ of a ‘system’ are related to, and are influenced by, its ‘inputs’.1
Effect on Response with change in Design Variable
Application of Sensitivity Analysis1:
Interaction between design variable(s) and response
Feature and structure selection and ranking in ML
Decision support system, MCDM
Multi-disciplinary optimization, etc.
Surrogate model
Sensitivity
Analysis Tool
Sensitivity
Analysis
Razavi, Saman, et al. "The future of sensitivity analysis: An essential discipline for systems modeling and policy support." Environmental Modelling & Software 137 (2021): 104954.
Fig. General framework of surrogate-assisted Sensitivity Analysis
Chart: 
| x_1 | x_2 | x_3 | x_4 | x_5 | x_n
Sales | 5 | 6 | 2 | 2 | 3 | 4

## Slide 4: Current Challenges
Curse of dimensionality1
  With increasing the dimension computational cost of meta-modeling increases
Accuracy of meta-model1
  Due to limited budget, the accuracy of the meta-modeling affected with increasing the dimension
Presence of discontinuities1
The definition of sensitivity i.e. is not defined at discontinuities
An efficient meta-modeling technique is required to-
  reduce the computational cost of meta-modeling
  increase the accuracy of meta-modeling
  identify the discontinuities present in the response function
  provide interaction among the design variables and response
Chart: Curse of Dimensionality
| 1 | 2 | 3 | 4 | 5
r = 1 | 2 | 3 | 4 | 5 | 6
r = 2 | 3 | 6 | 10 | 15 | 21
r = 3 | 4 | 10 | 20 | 35 | 56
Dimensions (n)
Number of coefficients (a)
Figure: Computational Cost for PRS
Figure: Discontinuous function
x
f (x)
x
f (x)
Figure: Error in meta-modeling
A
1. Cheng, Kai, et al. "Surrogate-assisted global sensitivity analysis: an overview." Structural and Multidisciplinary Optimization 61 (2020): 1187-1213.
B
Actual
Predicted
x = x0

## Slide 5: Self-Organizing Maps (SOM) 1/2
Training SOM
SOM Grid
Input data to SOM
Response:
DoE:
Figure: Working principle of Self-Organizing Maps (SOM)
Kohonen, Teuvo. "The self-organizing map." Proceedings of the IEEE 78.9 (1990): 1464-1480.

## Slide 6: Self-Organizing Maps (SOM) 2/2
45
30
15
Figure: Input variables and response representation through Self-Organizing Maps (SOM)
Initialization:
Random
Linear
Training:
BMU calculation
Weight update
Thole, Sidhant Pravinkumar, and Palaniappan Ramu. "Design space exploration and optimization using self-organizing maps." Structural and Multidisciplinary Optimization 62.3 (2020): 1071-1088.

## Slide 7: Proposed Methodology 1/2
STEP 1: Obtain SOM component planes using the data
STEP 2: Represent the input and response in a 2-d latent space,
STEP 3: Stack the data
STEP 4: Build meta-models for input variables in latent space
STEP 5: Build meta-model for response
……
Figure: Self-Organizing Maps (SOM) assisted Meta-modeling
SOM-assisted Meta-modeling
(0,0,3)
(0,0,3.25)
(0,0,1.7)
(0,0,21)

## Slide 8: Proposed Methodology 2/2
Fig. Proposed approach for SOM-assisted sensitivity analysis
SOM Component Plane (s , t)
Data: [x y]
x1(s , t)
x2(s , t) …
y (s , t)
Jacobian computation in SOM space
Sensitivity Analysis
Input
Obtain ()
Meta-modeling in SOM space
Mapping
Given: Data
Sensitivity Analysis:
Applying chain-rule
Sensitivity analysis through latent space
Where, is the pseudo inverse of the Jacobian Matrix
SOM-assisted Sensitivity Analysis
PRS Model:
Number of coefficient (a) to be estimated =
Without using SOM =
Using SOM =
Chart: Dimension (n)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Without SOM | 3 | 6 | 10 | 15 | 21 | 28 | 36 | 45 | 55 | 66 | 78 | 91 | 105 | 120 | 136 | 153 | 171 | 190 | 210 | 231
With SOM | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30 | 33 | 36 | 39 | 42 | 45 | 48 | 51 | 54 | 57 | 60 | 63
Chart: Dimension (n)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Without SOM | 3 | 6 | 10 | 15 | 21 | 28 | 36 | 45 | 55 | 66 | 78 | 91 | 105 | 120 | 136 | 153 | 171 | 190 | 210 | 231
With SOM | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30 | 33 | 36 | 39 | 42 | 45 | 48 | 51 | 54 | 57 | 60 | 63
Figure: Computational Cost (PRS degree r =2)
Design variable dimension vs. Computational cost

## Slide 9: Results 1/6 | Sphere Function
Sphere function1:
Inferences:
SOM plot provides essential information on response and variable interaction
Response is equally sensitive to the variable and
SOM-based meta-model provides good fit and sensitivity information
Benchmark Example
Molga, M., & Smutnicki, C. Test functions for optimization needs (2005). Retrieved June 2013, from http://www.zsd.ict.pwr.wroc.pl/files/docs/functions.pdf
Fig: Meta-model accuracy
Fig: Sensitivity information (-1,-1) to (1,1)
Fig: SOM plots for Sphere function
C
B
A
D
C
B
A
D
C
B
A
D
E
E
E

## Slide 10: Results 2/6 | Webster Function
Webster et al. (1996) function1:
Inferences:
Response is more sensitive to the variable than the variable
SOM-based meta-model provides good fit and sensitivity information
This sensitivity information can be used for feature selection
Benchmark Example
Webster, M. D., Tatang, M. A., & McRae, G. J. (1996). Application of the probabilistic collocation method for an uncertainty analysis of a simple ocean model
Fig: Meta-model accuracy
Fig: Sensitivity information
A
A
A
B
B
B
Fig: SOM plots for Webster et al. (1996) function

## Slide 11: Results 2/6 | Webster Function
Webster et al. (1996) function1:
Inferences:
Response is more sensitive to the variable than the variable
SOM-based meta-model provides good fit and sensitivity information
This sensitivity information can be used to quantify the non-linearity
Benchmark Example
Webster, M. D., Tatang, M. A., & McRae, G. J. (1996). Application of the probabilistic collocation method for an uncertainty analysis of a simple ocean model
Fig: Webster function
Fig: Sensitivity information (-1,-1) to (1,1)
Fig: SOM plots for Webster et al. (1996) function
C
A
B
C
C
C
A
A
A
B
B
B

## Slide 12: Results 3/6 | Short Column
Short Column function1:
Inferences:
Limit state function () is positively correlated with Yield strength () of material
is negatively correlated to moment of inertia () and applied load ()
SOM-based meta-model provides good fit and sensitivity information
Fig: Meta-model accuracy
Kuschel, N., & Rackwitz, R. (1997). Two basic problems in reliability-based structural optimization. Mathematical Methods of Operations Research, 46(3), 309-333
Engineering Example
Fig: Sensitivity information
Fig: SOM plots for Short Column function

## Slide 13: Results 4/6 | Knee Point in Pareto Front
Naru-Weiss problem1:
Inferences:
Near the knee point region, objective function is more sensitive
Near the knee point region, sensitivity order-
This information is crucial in multi-criteria decision making (MCDM)
Knee Point Identification
Fig: Knee point sensitivity information
Fig: SOM plots for Naru-Weiss Problem
Knee point
region
Knee point
region
Fig: Pareto front of Naru-Weiss problem
Knee Point
Miettinen, K., and M. M. Mäkelä. "Interactive bundle-based method for non-differentiable multi-objeective optimization: NIMBUS." Optimization 34.3 (1995): 231-246.
A
A

## Slide 14: Results 5/6 | Disjoint Pareto Front
DPF-4 problem1:
Inferences:
Objective and share negative correlation
Objective is more sensitive to as compared to the objectives and
The above information is crucial in reference direction-based MCDM
Sensitivity Analysis of Pareto Front
Fig: SOM plots for DPF-4
Fig: Sensitivity information in region ‘A’
Fig. Disjoint Pareto Front
Yadav, Deepanshu, et al. "Visualization-aided multi-criteria decision-making using interpretable self-organizing maps." European Journal of Operational Research 309.3 (2023): 1183-1200.
A
B
E
D
C
O
O
O
O
P
P
P
P
Q
Q
Q
Q
Direction | OP | OQ
Direction | OP | OQ
O
P
Q
O
P
Q

## Slide 15: Results 6/6 | High-dimension Problem
General Aviation Aircraft1:
  10 Objective functions and 27 design variables
  SOM-Kriging meta-models require less number of parameter estimation, hence requires less computational cost
  SOM-Kriging meta-models are more suitable for sensitivity analysis
Real-world Problem
 |  |  |  | SOM-Kriging |  |  |  |  | Kriging |  | 
 |  |  |  | X-val: Uniform Samples |  | X-val: LHS |  | % PrESS RMSE/Range | X-val: Pareto Optimal Solutions |  | 
 |  |  |  | RMSE | % RMSE/Range | RMSE | % RMSE/Range |  | RMSE | % RMSE/ Range | % PrESS RMS/Range
 |  |  |  |  |  | 0.29 | 14.07 | 18.97 | 0.65 | 31.59 | 28.65
 |  |  |  |  |  | 15.84 | 4.82 | 7.52 | 84.39 | 25.70 | 24.46
 |  |  |  |  |  | 2.84 | 6.59 | 14.72 | 10.65 | 24.73 | 22.84
 |  |  |  |  |  | 0.05 | 5.39 | 11.05 | 0.207 | 24.51 | 24.11
 |  |  |  |  |  | 10.53 | 3.28 | 7.51 | 77.68 | 24.21 | 23.10
 |  |  |  |  |  | 291.21 | 4.42 | 7.41 | 1580 | 23.99 | 22.56
 |  |  |  |  |  | 183.01 | 8.18 | 11.21 | 478.72 | 21.38 | 20.57
 |  |  |  |  |  | 0.47 | 7.07 | 9.96 | 1.58 | 23.74 | 23.37
 |  |  |  |  |  | 1.74 | 6.40 | 10.81 | 6.35 | 23.43 | 22.85
 |  |  |  |  |  | 0.95 | 20.23 | 9.75 | 0.89 | 19.18 | 18.89
 |  |  |  | SOM-Kriging |  |  |  |  | Kriging |  | 
 |  |  |  | X-val: Uniform Samples |  | X-val: LHS |  | % PrESS RMSE/Range | X-val: Pareto Optimal Solutions |  | 
 |  |  |  | RMSE | % RMSE/Range | RMSE | % RMSE/Range |  | RMSE | % RMSE/ Range | % PrESS RMS/Range
 |  |  |  |  |  | 0.29 | 14.07 | 18.97 | 0.65 | 31.59 | 28.65
 |  |  |  |  |  | 15.84 | 4.82 | 7.52 | 84.39 | 25.70 | 24.46
 |  |  |  |  |  | 2.84 | 6.59 | 14.72 | 10.65 | 24.73 | 22.84
 |  |  |  |  |  | 0.05 | 5.39 | 11.05 | 0.207 | 24.51 | 24.11
 |  |  |  |  |  | 10.53 | 3.28 | 7.51 | 77.68 | 24.21 | 23.10
 |  |  |  |  |  | 291.21 | 4.42 | 7.41 | 1580 | 23.99 | 22.56
 |  |  |  |  |  | 183.01 | 8.18 | 11.21 | 478.72 | 21.38 | 20.57
 |  |  |  |  |  | 0.47 | 7.07 | 9.96 | 1.58 | 23.74 | 23.37
 |  |  |  |  |  | 1.74 | 6.40 | 10.81 | 6.35 | 23.43 | 22.85
 |  |  |  |  |  | 0.95 | 20.23 | 9.75 | 0.89 | 19.18 | 18.89
Table: SOM-assisted meta-modeling on General Aviation Aircraft problem demonstrating the effectiveness of proposed approach for high dimensional problem
Simpson, Timothy, et al. "Conceptual design of a family of products through the use of the Robust Concept Extrapolation Method." 6th Symposium on Multidisciplinary Analysis and Optimization. 1996.

## Slide 16: Summary
Discussed the current challenges in meta-modeling based sensitivity analysis
Proposed Self-Organizing Maps (SOM) assisted meta-modeling
Proposed SOM for sensitivity analysis to address the current challenges
Demonstrated the proposed approach on benchmark analytical and real-world engineering problems
Limitations and challenges
  Topographic error and quantization error should be very less
  Jacobian in input space shouldn’t be close to zero
Suggestions
  The latent dimension can be more than two i.e. for reducing the error of meta-modeling
  A parametric study on accuracy of meta-model in SOM space with map size is needed
Future work
  Comparison of proposed method with existing techniques for sensitivity analysis
  An unified framework for SOM-based sensitivity analysis for various applications

## Slide 17: Thank You!
Open for questions!!
email: deepanshu.yadav380@gmail.com

## Slide 18: Other presentations from our lab
Name | Title | Session | Date and Time
Mr Pranjul Dubey | Online Fault Detection in Machine Parts Using Motif Discovery and Dynamic Time Warping | Parallel Session 4: Data-driven methods 2 | 6 June 16:30 – 18:00 (17:10) Room: Cummins G10
Mr Kannan Sekar | A novel multi-objective optimization formulation for strain variance optimization in isothermal forging | Parallel Session 2: Novel Methods for Modelling, Simulation, and Design 3 | 8 June 11:20-12:50 (12:00) Room: Boole 4